## Slide 2: Mempolicy Is Dead Long Live Memory Policy Gregory Price

## Slide 3
What’s the story here?
“I have special memory and I don’t want to use it like memory. I want malloc().”
~ Many $DEVICE_DEV for many $REASON.
“Don’t put the memory in the page allocator…”
~ Many $KERNEL_DEV for many $REASON.
(good $KERNEL_DEV, good $REASON)
Corollary: “also you must re-implement everything in mm/”

## Slide 4
What do we do instead?
DAX
  The X shaped device goes in the DAX shaped hole
  A decade later: Promise of userland allocators never materialized
HMM / ZONE_DEVICE migration
  complexity, overhead - still limited core services
People shove it in the page allocator anyway
  Platform can just set EFI_CONVENTIONAL_MEMORY
  memory as NUMA node in ZONE_NORMAL (worst case)
  page_alloc, reclaim, compaction end up using this to poor effect.

## Slide 5
What are the use cases?
For some classes of memory, want mm/ services w/ alloc & access controls
GPU / Accel memory
  Don’t want spillage.
  Might want reclaim / compaction / PT controls
Compressed Memory device
  Want really hard write-access controls to prevent fatal OOM
  Want most mm/ services
Slow (X00ns+) / Contended BW Memory (Large memory pool)
  Don’t want in the fallback list.
  Do want demotion and promotion.
  Do want reclaim, compactions, probably hotplug.

## Slide 6
What does [in the page allocator] mean?
Object — member of —> Object
Page —> Memory Zone
Zones —> Memory Node
Memory Node —> node_states[N_MEMORY]
page_alloc default memory policy (nid=NUMA_NO_NODE, nodemask=NULL):
(zone < DEVICE) for node in node_states[N_MEMORY]
Take away: in the page allocator = in N_MEMORY

## Slide 7
What about existing policy mechanisms?
cgroup.cpusets.mems_allowed
allows you to restrict node access for tasks in a cgroup hierarchically
if cpuset.mems=[0], those tasks can only access node 0.
Removing node from root.mems prevents everything* from accessing a node.
Not isolating the root means root tasks may access the node. Insufficient as-is.
mempolicy
completely disregarded by a variety of mm/ services (reclaim, migration)
Can be overridden by unprivileged userland actions
Per-task, Per-VMA. Way too much surface area.
*except certain contexts like interrupts

## Slide 8
Memory Arenas: N_MEMORY, N_SPM
“It would be nice if the page allocator could operate on different Arenas.”
$KERNEL_DEV said this to me off hand in a meeting one day
I demonstrated this in my RFC for this talk: Specific Purpose Memory Nodes
cpuset extension
memory-tier/hotplug provide exclusive nodelists (proper solution: N_SPM)
GFP flag
Similar mechanism had previously been proposed, Twice
essentially adds N_SPM
Opinion: I think between these two proposals, we have the full puzzle.

## Slide 9
How it works
N_SPM and N_MEMORY do not intersect
  All current users of page_alloc default to using N_MEMORY
  page_allocator hard-filters nodemask on N_MEMORY
cpusets.mems_allowed operates on UNION(N_SPM, N_MEMORY)
  a new (non-user facing, internal) cpusets.sysram_nodes provides N_MEMORY filter equivalent
GFP_SPM_NODE flag provides a switch to change the filter function
  when flag is present, filter on N_SPM instead of N_MEMORY
  when flag is present, filter on mems_allowed instead of sysram_nodes
This essentially creates “Private Memory Nodes”
Names are hard: Specific Purpose vs Private - same thing?

## Slide 10
What then?
Maybe pivot ZONE_DEVICE to but used for this.
  allow things like page_is_spmem() similar to devmem page checks
  allows clean callback into driver to push complexity out of core kernel
enlightened drivers that register SPM nodes and can alloc, free, and manage access constraints (Page Table perms, maybe re-use hmm code here).
do not extend mempolicy or other user-facing components to be SPM aware
  forces complexity into drivers.
  limited userland exposure means lower long-term risk

## Slide 11
FAQ
What not just use mempolicy?
  insufficient isolation and explicitly ignored by a variety of users.
Can’t we just manage with existing cgroups extensions?
  not all systems use cgroups or cpusets
  root can’t remove the node (nothing will be able to access at all)
Do we really need the GFP flag?
  yes… no… maybe.
  Provides a much harder isolation guarantee and fewer tripping hazards.
Why not ZONE DEVICE?
  Still have to re-implement core services like reclaim (if wanted)
  Can imagine SPM_NODE using ZONE_DEVICE, so think of this as another ZONE_DEVICE mode?