## Slide 1: Unordered I/O (UIO) and P2P paths in CXL
Arun George

## Slide 2: Outline
PCIe UIO
CXL leveraging UIO
Kernel integration aspects
What does an MVP look like?

## Slide 3: PCIe vs. PCIe with UIO (Unordered I/O)
PCIe (Conventional)
PCIe with UIO (Unordered I/O)
⚠ Fabric-Enforced Ordering
• One valid path only (tree topology) — limits scaling to multi-path/multi-link fabrics
• Single upstream port per device/switch caps bandwidth; no independent P2P path
⚠ No Write Completions
• Writes have no end-to-end acknowledgment — source can't tell if/when a write lands
• Forces the fabric to enforce ordering everywhere, to keep data consistent
⚠ Queue Backpressure
• Transactions share queues/buffers and can't bypass a stalled packet ahead of them
• A slow destination's backpressure spreads to unrelated flows (tail latency)
✓ Source-Managed Ordering
• Scales with multi-path, multi-link fabrics — distinct paths are inherently unordered
• Direct P2P and independent paths become possible; end-points enforces order, not the fabric
✓ UIO Writes Get Completions
• Every UIO write returns a completion — end-to-end acknowledgment
• Requester delays the “flag” write until data-write completions arrive
✓ Reduced Head-of-Line Blocking
• Independent operations bypass a stalled path; dedicated VC keeps UIO off legacy queues
• The requester only waits where a real ordering dependency exists
Fabric-Managed Ordering
Source-Managed Ordering
Sources: PCIe UIO ECN (PCI-SIG, final Mar 2023); PCI-SIG Educational Webinar “Unordered IO for Improving Performance and Efficiency of PCIe Fabrics for AI/ML Applications” (D. Das Sharma, Intel & S. Glaser, NVIDIA — PCI-SIG Board.
PCIe v6.1 introduced Unordered IO feature

## Slide 4: What UIO Requires (Prerequisites)
Flit Mode along the path
All links on the requester-to-completer path use PCIe 256-byte Flit Mode.
Streamlined Virtual Channel (SVC)
TC3/VC3 required for UIO. TC4/VC4 optional. Conventional traffic remains separate.
Requester and completer support
Device 3 capability advertises support. Software enables a usable path.
14-bit tags
A larger identifier space for outstanding operations. Actual concurrency varies.
UIO is optional. A PCIe generation label alone does not establish support.
Notes: This behavior requires support along the actual requester-to-completer path.
A capable GPU by itself is not sufficient.
First, the links on that path need PCIe Flit Mode.
We also need the virtual-channel support and configuration that carry UIO separately from conventional traffic.
The checklist here includes the Streamlined Virtual Channel capability,
with TC3 and VC3 for the required UIO channel and an optional additional channel.
At the endpoints, the requester and completer must advertise the appropriate capability.
Software must enable the requester only for a path that can support the transactions.
The Device 3 capability exposes the relevant support and control information.
The larger tag space helps identify outstanding operations and their completions.
The implemented queues and credits still determine how much concurrency a particular device can sustain.
One important deployment point is that a PCIe generation number is not enough to establish UIO support.
We need to discover the actual capabilities and configure the path.
Conventional traffic also remains necessary for ordinary device operation.
This is already a software problem: enumerate the components, determine whether the route is usable, and keep that decision valid for the lifetime of the mapping.

## Slide 5: UIO in CXL: P2P to HDM for non-CXL xPUs
UIO Direct P2P to HDM over cxl.io
  Carry the request on CXL.io against an HDM region rather than a BAR-mapped MMIO window
  The requester needs UIO on CXL.io.
Peer access to HDM region over existing protocol
  Earlier: CXL.mem gives the host a coherent access to device memory, but a peer device reaching that same HDM region had to go through the host
  Now: UIO gives CXL a P2P path to HDM over the existing CXL.io/PCIe transport.
Formalized in CXL spec v3.2.
CPU
CXL Host Bridge
CXL
CXL Switch
Non-CXL GPU
PCI

## Slide 6: UIO in CXL: use cases
CXL as Host Managed
  Host CPU (applications/kernel) is the owner of CXL region
  P2P data need to be coherent with CPU
  ** Coherency is important; host should see the pages **
CXL as a Memory Expander for GPU
  GPU is the owner of this CXL region
  Host applications need not bother about this data.
  ** Coherency is not important; host need not see the pages **

## Slide 7: Linux Kernel: What to consider for UIO?
Linux Kernel: Control path
  HW does the heavy lifting and achieves the unordered IO transactions.
  SW enumerates, manages life cycle, provisions etc.
  Life cycle management :The kernel helps a UIO-capable P2P route to be discovered, committed, and torn down.
Key aspects to be considered:
  Consumption of UIO capability: PCI/CXL/P2PDMA layers need to consume UIO capability and provision it.
  UIO route management: Feature capability in the entire route and life cycle management
    A UIO-capable route isn't just reachability, checked once; every node from requester to provider must actively hold UIO enablement for the entire lifetime of the route.
    Then the possibility of multiple routes in non-hierarchical topologies.
  Host-coherency management: (Host-Managed or Memory Expander for XPU cases)
    Sometimes host coherency is ensured through Back-Invalidation (BI); when it isn't, software has to ensure it explicitly for host-managed case.
Notes: Now let’s dig a bit further on Linux kernel aspects now.
Hardware does the heavy lifting for UIO transactions, but software – kernel - is also required for the control path and life cycles of routes.
Kernel enumerates the UIO capabilities, manages the life cycle and provision the feature to the consumer modules.
When we say life cycle, it means a UIO capable route has to be discovered, committed and torn down when something goes down.
So, some of the key aspects to be considered here are:
- consumption of UIO capability: There are different layers in kernel which need to consume the UIO capability, and provision this capability for any upper or peer layers who want to leverage it further. In this CXL use case, we will talking about CXL, PCI and P2P DMA layers.
- And the route management: The UIO capable route detection and it’s life cycle management is a key aspect for UIO, since the capability need to ensured for the entire route.
Then there is the possibility of multiple routes in non-hierarchical topologies which is one of the main aspects of UIO feature.
- Then with CXL, we need to see the host-coherency management. Some accelerator or GPU might have done the P2P transfer to the CXL memory. Now how to consume it? Or is there any need to consume it?
If host/CPU need to consume it, how will we ensure coherency?
These are some of the questions an ecosystem developer need to ponder. We will discuss the possible approaches to solve these challenges.

## Slide 8: Linux Kernel Approach for UIO
UIO legality is formed by a tuple (requester, path, target set, address range), aka the route.
UIO enablement spans three layers:
  PCIe
    SVC/UIO Enumeration (discover SVC/Flit-mode/DevCap3 capability)
    Route building (build and validate the requester-to-completer route)
  CXL
    Detect HDM decoder capability, provision HDM regions with UIO
    Coherency management with Back Invalidation (BI).
  P2PDMA
    Enable UIO capability to providers and requesters, manage life cycle of routes.
CXL HDM UIO
HDM capability, region provisioning, coherency
PCIe UIO
route discovery, SVC/Flit enablement
P2PDMA Providers
BAR MMIO / UIO-only / CXL-HDM
RDMA
GPU drivers
Block / NVMe-oF
VFIO / iommu-fd
uses
HW Enabling
Consumer modules
Provisioning
PCI UIO state:
SVC, Flit, Dev3
HDM UIO state:
decoder cap
P2P UIO state:
Req / Provider cap
dma_buf or scatter list
Notes: This gives an idea of minimal viable product if we enable the ecosystem.
Our CXL UIO use case spans three layers mainly – pci, cxl and p2pdma.
In PCIe, we do the SVC and UIO enumeration and capability checks like flit mode etc. These are the mandatory building blocks on which UIO feature is built. We make sure that the given port satisfy all those requisites.
PCI layer also need to provide the support infra for route building and management. When I say the route, it is the fully UIO capable shortest route from p2p requester to provider.
In CXL, we need to detect HDM capability for UIO, and provision the HDM memory regions as UIO capable.
Then coherency need to be managed as we discussed earlier.
In p2p layer, we will provide UIO capability for providers and requesters or consumers. We make sure that dma mapping is enabled in the right way particularly while dealing with the CXL HDM regions, whether we use dma_buf or conventional scatter lists to expose buffers and so on. And we need to take into account the iommu aspects, whether it can support UIO transactions or not. Sometimes we will have to use the iommu passthrough route mandatorily for uio.
In the diagram, we can also see the requester modules on the top which will typically make use of the UIO enabled routes, which could be rdma, gpu drivers etc.

## Slide 9: Some UIO implementation details…
CXL Region with UIO
PCIe UIO
route discovery, SVC/Flit enablement
P2PDMA Providers
BAR MMIO / UIO-only / CXL-HDM
uses
struct pci_uio_state {
u32 svc_cap;
u8 num_vcs;
unsigned int uio_requester:1;
unsigned int uio_completer:1;
unsigned int uio_14bit_tag_cpl:1;
unsigned int uio_svc_vc3:1;
unsigned int uio_svc_vc4:1;
unsigned int enabled:1;
unsigned int uio_req_enabled:1;
struct pci_svc_vc_state svc_vcs[];
};
CXL HDM Decoder with UIO
struct pci_svc_vc_state {
u8 vc_id;
u8 tc_map;
unsigned int available:1;
unsigned int enabled:1;
unsigned int negotiated:1;
};
struct cxl_hdm_uio_state {
bool capable;
bool enabled;
unsigned int decoder_count;
u8 supported_coherency;
};
Region level UIO cap advertising
Target interleaving settings for UIO
Coherency Models:
CXL_HDM_DECODER_COHERENCY_DEV
CXL_HDM_DECODER_COHERENCY_HOST
CXL_HDM_DECODER_COHERENCY_HOST_BI
struct pci_uio_route {
struct kref ref;
struct pci_dev *requester;
struct p2pdma_provider *provider;
const struct pci_uio_route_ops *ops;
unsigned int nr_hops;
struct pci_dev **hops;
unsigned int nr_targets;
struct pci_dev **targets; ……
#define DMA_ATTR_UIO ...
Declares that the device may access this mapping using PCIe Unordered * IO semantics.
Notes: This slide gives a bit more implementation details.
You can see three data structures depicting the three layers involved.
Cxl_hdm_uio_state: involves the hdm state interms of uio
Pci_uio_state: uio/svc capabilities of the associated pci port entity
Pci_uio_route: This comes in the next level: An object which indicates the route and its management.
We also will have to introduce a few semantics for DMA operations. Either resusing the dma_ops or exposing it as dma_buf and so on.

## Slide 10: New P2P Provider types
P2P Providers with different mapping policies
  PCI_BAR_MMIO: conventional P2P capable PCI BAR regions
    Does not support UIO mode
  PCI_UIO: PCI BAR regions with UIO capability
    New concept: could be backed by any UIO capable PCI entity. Typically, data is consumed by device
  CXL_HDM_UIO: CXL HDM memory regions which can support cxl.mem and P2P UIO cxl.io accesses
    New concept: A CXL HDM region which is host-controlled, and data is consumed by host (unless type 2)
    Since HDM regions are not static mapping like PCI BARs, some kernel features like iommu support might be impacted.
    Bring in host-coherency related aspects such as Back Invalidation.
CXL_HDM_UIO
Switch /
Root Port
Host
Requester
PCI_UIO
PCI_BAR_MMIO
XPU
XPU
Data Consumption
Notes: With UIO in place, software has to model different P2P provider capabilities.
One way to do that is give here:
PCI_BAR_MMIO: gives the regular mapping
PCI_UIO: it indicates the PCI BAR mappings with UIO capability. This could be reached by means of Gen 6 PCI switches or host bridges.
CXL_HDM_UIO: These are the rpoviders which support cxl or p2p uio cxl.io accesses.
It will have a different access control rules than PCI regions. Ex: It can be reached only through cxl switches or CXL host bridges since it requires HDM decoder support.

## Slide 11: Accessing CXL HDM regions: Coherency Management
Does the data to be coherent with host?
  ‘Yes’ for Host-Managed case.
  ‘No’ for Memory Expander for XPU case.
In Host-Managed case:
  A typical UIO P2P transfer to CXL require the data to be consumed by host applications
  Ex: A CXL type 3 region is always consumed by host
  The exception could be CXL type 2 devices where device consumes the data
The P2P requester might want to choose:
  Is this transfer kept coherent with the host's view of that memory, or not?
  If coherency not available in the platform, requester/provider has to ensure coherency itself (in Case A):
    Explicit cache-line flush around the access window, plus a memory barrier.
  This SW fallback is an optional workaround with an overhead
Is the CXL region BI-capable?
Yes
Hardware Back-Invalidation snoops
maintains coherency automatically
No
Software must ensure coherency:
explicit cache-line flush + barrier
P2PDMA UIO
CXL Region
CXL HDM
Coherency models
Notes: Moving on to the next topic:
This is on the coherency management for CXL HDM regions.
Does the data need to be coherent with the host, ie CPU? We believe, yes for most use cases.
A CXL type 3 device’s data need to be consumed by host application in most cases.
So p2p requester might have to be aware of the coherency capabilities, and might want to ensure that that the data is persisted with host in a coherent manner.
CXL HDM-DB regions, which are the regions with Back invalidation support gives the host a hw level support for the same.
If BI is not supported, the kernel might have to do the explicit cache flush instructions to ensure coherency.
In an alternative model, we don’t have to ensure coherency. Data is not going to be consumed by host applications. Data is always consumed by the accelerator who writes it. It could be using this area for capacity expansion.

## Slide 12: Accessing CXL HDM regions: ZONE_NORMAL / ZONE_DEVICE?
P2P to HDM region
  Every existing P2PDMA/RDMA/GPU-driver provider assumed the target device was MMIO BAR.
  HDM is different — coherent memory behind a CXL decoder — and the difficulty depends entirely on how that memory region is exposed in the kernel.
Case A — As ZONE_DEVICE (devdax): less complex one.
  CXL driver can map HDM into `ZONE_DEVICE pages (existing pci_p2pdma_add_resource() method).
  This is like existing P2P regions mapping
    The regions will not be available for Kernel allocations. Only the P2P requesters and explicit memory mapped applications will access it.
  It serve well for “CXL as a Memory Expander for xPU” use case.
  It is bit unclear for “host-managed” case.
    It might make sense for a CXL type 2 device where the data will be consumed by the accelerator inside it. But may not be for type 3.
Notes: Now comes to another software aspect of accessing HDM regions as P2P targets.
How do we expose these regions?
Case a is less complex of the cases: as ZONE_DEVICE mappings.

## Slide 13: Accessing CXL HDM regions: ZONE_NORMAL / ZONE_DEVICE? …
Case B — As kernel managed ZONE_NORMAL / MOVABLE (system-ram):
  The default, regular case for CXL memory regions. User and kernel spaces can see and consume.
  Once onlined as system RAM, HDM pages are indistinguishable from regular RAM to the allocator
    Subject to reclaim, swap, and migration, with no `pgmap`-based isolation.
    Pages are migration targets here, so a P2P enabled page must be excluded from migration for the whole pin duration.
    Page must be pinned first (FOLL_LONGTERM?) before it can be a P2P target
  Potential approaches:
    Ownership model: p2p uio model establish an ownership model which prevents hot-unplugging of these regions while DMA is ongoing
    Private node approach: should we keep UIO CXL HDM region as ‘private node’ memory?
      This approach provides isolation and different memory policies, while still being ZONE_NORMAL
  Takeaway: ZONE_NORMAL / MOVABLE looks to be the plausible method for consuming CXL HDM region like a regular RDMA memory.
    Might serve the ‘host-managed‘ case better.
    But, enabling challenges would be more
Notes: The other case is a bit more interesting.
This is the regular mode for CXL memory regions where it is added as ZONE_NORMAL or ZONE_MOVEABLE. User and kernel spaces can see and consume it.
The problem is, once onlined, it is indistinguishable from a regular RAM for the page allocator.
It would be subject to reclaim, swap, migration etc. with no isolation in place. So it need to be explicitly excluded from those operations.
Also we need to pin the pages to become a p2p target.
So a couple of approaches could be tried here.
An ownership model for these p2p uio pages can be built which prevents it from migration, hot unplug etc.
Other interesting approach in this direction is the Private node memory approach which is recently being discussed in MM communities.
The takeaway is that this method looks to be promising but there are a number of challenges.

## Slide 14: Accessing CXL HDM regions ..
Case C: DMA_BUF
  ZONE_DEVICE based isolation or ZONE_MOVABLE can still be applied.
  Coherency models can be integrated more easily with dma_buf
    With dma_fence(?) callbacks and coherency workers if needed
  Challenges:
    The consumption model for the use cases need to be built. Is it Host-managed or capacity expansion for xPUs?
  Takeaway: DMA_BUF is an interesting option for UIO use case integration
Notes: DMA_BUF infra provides another interesting option to build the upper layer use case integration infra.
Both ZONE_DEVICE and ZONE_MOVABLE models work here.
And coherency models (HW supported with Back invalidation or SW ones) can be integrated
A few challenges remain though.
The consumption model for use cases need to built. Is the application supposed to consume the data? Or is the region meant as a capacity expansion for the accelerator who uses it?
And is it ZONE_DEVICE or ZONE_MOVABLE?
The key takeaway is that it is an interesting for use case itegration

## Slide 15: Life management of UIO routes
Why UIO routes are different from normal P2P routes?
  Regular P2P routes
    Are tree-based (hierarchical)
    Address is enough to establish path
  UIO Routes
    Can be non-hierarchical. Multiple paths can exist b/w requester and provider
    Address is not enough to establish route. All nodes in the route should be UIO capable.
  Why life management of UIO routes?
    Changes in UIO mode: any change in UIO capability of nodes can make the established route non-valid
    So it calls for a new design to establish and maintain UIO routes.
Target
Switch
Host
Requester
Target
Switch
Host
Requester
Multiple paths
Conventional P2P path
Typical UIO P2P path
Notes: We will get a bit more into the life management of routes.
Why UIO routes are different from regular p2p routes? Why it has to be managed differently.
A few points:
Regular p2p paths are tree based ones, that is hierarchical and will have a root port.
And address is enough to establish the path, since only one valid path exisits between the requester and provider.
But UIO routes can be non-hierarchical, and there could be many valid paths.
And address is not enough to establish the route. All the nodes in the route need to be UIO capable.
So any change in the UIO capability in the nodes or any node reset can make the route invalid.
And the consumers of this route need to be properly notified on these changes.
These calls for a new design to establish and maintain the UIO routes.

## Slide 16: Life management: Route object
Route object
  Tracks all nodes on the path from requester to provider
  Reference counted, revocable
  Has a life which depends on the state changes on nodes
  Invalidated by any event that can no longer guarantee support along the path (hot-remove, link-down, capability loss)
  There can be multiple route objects from requester to provider
Target
Switch
Host
Requester
Route A
Route B
Target
Switch 1
Host1
Requester
Host2
Switch 2
A simpler topology
More complex topology
Notes: So we add a route object entity for this management.
It tracks all the nodes from requester to provider.
It is reference counted entity.
It has a life which depends the state changes on the node. Certain state changes which non-longerr gurantee uio support will invalidate the route.
There could multiple route objects between a pair of nodes.

## Slide 17: Route acquisition
Valid reference:
Capabilities: requester DevCap3.REQ, provider UIO_COMPLETER.
range_valid(): cxl resolves the subrange to its interleave target set and granularity.
Per-target walk up to the lowest common ancestor (LCA): flit mode per link, SVC routing per hop, ACS-free path (BAR) or ATS-capable requester (HDM).
Commit, leaf -> requester, unwinding in reverse on any failure.

## Slide 18: End-to-end lifecycle
1) Probe
cxl_pci/cxl_mem probe
cxl_bi_setup()
cxl_hdm_uio_setup() // cxlds->uio from DevCap3.CPL + HDM decoder cap
2) Provision
region created, uio=1 (pre-commit) decoders programmed (UIO bit, UIG/UIW), region becomes a typed provider
3) Acquire
pci_p2pdma_map_info() -> pci_uio_route_get() path validated, VC3 + requester enable committed leaf-to-requester
4) Map
dma_map_phys(..., DMA_ATTR_UIO [| MMIO for BAR])
6) Teardown
1. driver blocks new submissions
2. requester drains outstanding UIO completions
3. dma_unmap_phys() - the DMA core still never
4. pci_uio_route_put() - final put drops
5. region uncommit (echo 0 > commit) – provider gone;
5) Transfer (hw)
Init
Live
Destroy

## Slide 19: What does an MVP look like?
What is required for first stage ?
  What use case serve better for first stage?
What are ‘must have’ and ‘good to have’ features?
  PCI enumeration
  CXL enumeration
  CXL Region provisioning
  PCI route setup with UIO
  P2P DMA setup (scatterlist or dmabuf)?

## Slide 20: QEMU: Modeling a UIO-Capable Topology
QEMU allows developers to experiment while the actual HW matures.
Current state
  An RFC patch series on qemu-devel — “hw/pci: hw/cxl: Add UIO support in CXL and PCIe stack.” by Shrihari E S (August 2026) — adds UIO/SVC modeling to QEMU's PCIe and CXL subsystems.
  Scope — enumeration and configuration: SVC capability, Device3 capability, Flit-mode, HDM-decoder/DVSEC UIO advertisement and data-plane support.
  Status — RFC, under review by QEMU/CXL/PCIe maintainers, not yet merged.
RFC V1: UIO enumeration enablement patch series: [RFC 0/8] pci: cxl: Add enumeration support for Unordered I/O (UIO) feature
  Enables Flitmode in PCIe subsystem
  Enables UIO SVCs support in both CXL and PCIe subsystem
  Adds UIO support in CXL HDM decoder
RFC V2: UIO enumeration + Data path enablement patch series: [RFC V2 0/9] hw/pci: hw/cxl: Add UIO support in CXL and PCIe stack
  Adds SVC as a generic capability (RFC V1 adds SVC as a UIO centric capability)
  Plumbs Device3 capability support in PCIe subsystem
  Enables UIO related DVSEC registers intended for data plane support
Notes: Difference: RFC v2: SVC was added as a generic capability, and built UIO on top of it. While the earlier RFC V1 used SVC as only a means to enable UIO.

## Slide 21: QEMU: Modeling a UIO-Capable Topology
cxl_uio_test.ko
  Exercises the whole UIO consumer contract from debugfs.
  Guest test harness drives it: provider lookup from a committed region, pci_p2pdma_map_info() with all three policies, attribute derivation, dma_map_phys(), route validity and quiesce/revoke ops.
/sys/kernel/debug/cxl_uio_test/
requester (rw) requester BDF, e.g. 0000:10:00.0
region (rw) cxl region device name, e.g. region0
policy (rw) forbidden | preferred | required
offset (rw) subrange start offset into the region
len (rw) subrange length (0 = whole region)
acquire (w1) run map_info + map; (r) result dump
release (w1) unmap + route put
misuse (w1) deliberate DMA API misuse for dma-debug UIO
valid (r) current route validity
events (r) quiesce/revoke callback counters

## Slide 22: QEMU: Modeling a UIO-Capable Topology
Discovery in the guest
  # cat /sys/kernel/debug/pci_uio/capabilities
  0000:0c:00.0: routing
  0000:0d:00.0: routing
  0000:0e:00.0: routing
  0000:0e:01.0: routing
  0000:0f:00.0: requester completer routing
  0000:10:00.0: requester completer routing
Provision UIO region on mem0
  cd /sys/bus/cxl/devices
  region=$(cat decoder0.0/create_ram_region)
  echo $region > decoder0.0/create_ram_region
  echo 256 > $region/interleave_granularity
  echo 1 > $region/interleave_ways
  echo $((256<<20)) > $region/size
  echo ram > decoder3.0/mode
  echo $((256<<20)) > decoder3.0/dpa_size
  echo decoder3.0 > $region/target0
  echo 1 > $region/uio # pre-commit only
  echo 1 > $region/commit
  cat decoder3.0/uio # -> 1
3. Acquire a route and map it (mem1 requester, mem0’s region as target.
  cd /sys/kernel/debug/cxl_uio_test
  echo -n 0000:10:00.0 > requester
  echo -n region0 > region
  echo -n required > policy
  echo 1 > acquire
  cat acquire
  map_type: 3 PCI_P2PDMA_MAP_BUS_ADDR (in-fabric,
  peers emit HPAs, bus_offset 0)
  xport_uio: 1
  attrs: 0x4000 DMA_ATTR_UIO, no DMA_ATTR_MMIO
  route_tc: 3 default UIO TC/VC assignment
  route_vc: 3
  route_flags: 0x1 PCI_UIO_ROUTE_IN_FABRIC
  max_write_size: <path min MPS>
  boundary: 256 256B rule, clamped to interleave gran
  update_granule: 64 normative
  nr_hops: 3 dsp1, us0, dsp0
  nr_targets: 1