## Slide 1
A Thermal governor for hardware temperature control
Srinivas Pandruvada — Intel
Source Link (RFC)

## Slide 2
Today we mitigate temperature by proxy
Linux does not control temperature
  Controls frequency and/or power
    SoC power management controller takes action
Controls
  In band and out of band
    Different latency
    Own idea of what "one step" means
• All of them end up at the same microcontroller
  • Regulate temperature itself, far finer and faster: it owns the actuators
  Can coordinate several of them at once
2

## Slide 3
Why software stays in the loop: the sensor
Scenarios
  Case1:
  Sensor wired to the controller loop is self-contained —
  or reached via the EC → the OS only picks the target
  Case 2:
  sensor outside it: I2C / SPI only the OS can read it —
  thermistor, board or skin → the OS must feed it in
  sensor behind another bus
  Case 3:
  virtual / synthetic sensor: it does not exist in hardware —
  weighted mix of sensors, → the OS computes it, so only the OS
  model or firmware-derived can ever supply it
• Case 1 needs one value from Linux: the threshold
• Cases 2 and 3 need two: the threshold, and the temperature forever
5

## Slide 4
Today (With Intel PTC)
PTC: Platform Temperature Controller
sensor ──► thermal zone ──► sysfs ──► daemon ──► ptc_N_control
│ (MMIO)
└── must poll and re-push
the temperature forever
• Every consumer re-implements the feed
• Daemon dies → the loop keeps running on a stale override
• Suspend/resume re-programming is the daemon's problem too
• Trip points, hysteresis, zone lifetime: all duplicated in user space
6

## Slide 5
Proposal: a governor
user space
┌────────────────────────────────────────────────────────────┐
│ echo hardware > thermal_zoneN/policy │
│ thermal-threshold add N 80000 (netlink, THRESHOLD_ADD)│
└────────────────────────────────────────────────────────────┘
│
▼
┌────────────────────────────────────────────────────────────┐
│ thermal core │
│ __thermal_zone_device_update() │
│ ├─ get_temp() ──► tz->temperature │
│ ├─ handle trips, thresholds │
│ └─ governor->manage(tz) ──┐ │
└───────────────────────────────┼────────────────────────────┘
▼
┌────────────────────────────────────────────────────────────┐
│ gov_hardware — policy "hardware" │
│ │
│ lowest threshold of the zone ────► set_threshold() │
│ tz->temperature, every update ───► set_temperature() │
│ │
│ no cooling devices, no throttling decisions │
└───────────────────────────────┬────────────────────────────┘
│ thermal_hw_gov_ops
▼
┌────────────────────────────────────────────────────────────┐
│ platform_temperature_control.c │
│ TARGET_TEMP + ENABLE TEMPERATURE_OVERRIDE (+EN) │
└───────────────────────────────┬────────────────────────────┘
▼
┌──────────────────────────┐
│ HW control loop (PTC) │
└──────────────────────────┘
7

## Slide 6
Why a governor? Why not a cooling device?
set_cur_state(cdev, N): No Temperature input
  To make it fit you would bind the cdev to a trip and let some governor decide N
    A Linux control loop driving a hardware control loop. That is the thing we are trying to remove.
A governor is the framework's existing answer to "who owns mitigation for this zone":
  policy is mutually exclusive by construction
    selecting hardware guarantees no other algorithm touches the zone.
  manage() is called on every zone update
    with the temperature already read and trips already handled.
  bind_to_tz / unbind_from_tz
    give ownership lifetime for free.
  No new user-space ABI
    Policy, available_policies, trip_point_M_temp.
8

## Slide 7
The interface
struct thermal_hw_gov_ops {
int (*set_threshold)(void *priv, struct thermal_zone_device *tz,
int temp);
int (*set_temperature)(void *priv, struct thermal_zone_device *tz,
int temp);
};
struct thermal_hw_gov_dev *
thermal_hw_gov_device_register(const struct thermal_hw_gov_ops *ops,
void *priv);
void thermal_hw_gov_device_unregister(struct thermal_hw_gov_dev *hdev);
int thermal_hw_gov_device_zone_id(struct thermal_hw_gov_dev *hdev);
• Two values, two callbacks. That is the entire contract
• THERMAL_TEMP_INVALID threshold = "stop the loop"
• The zone is passed in for identity and future parameters
• Callbacks run under tz->lock — must not re-enter the thermal core
9

## Slide 8
Binding model
Hardware registers instances into a pool. Zones claim from it
registered instances thermal zones
┌──────────────┐
│ ptc_0_control│◄──── claimed ──── thermal_zone3 policy=hardware
├──────────────┤
│ ptc_1_control│ free
├──────────────┤
│ ptc_2_control│ free
└──────────────┘
• Claim happens lazily on the first zone update → registration order vs. policy-write order does not matter
• Released on policy change, zone teardown, or driver unbind
10

## Slide 9
Where the two values come from
Threshold — lowest netlink threshold of the zone (THRESHOLD_ADD, WAY_UP only)
  User space owned, no driver support needed — every zone has thresholds. The add ends in __thermal_zone_device_update(), so the target is programmed synchronously
  A writable trip point is a fallback only: those are often firmware backed (int340x: ACPI PATx)
Temperature — pushed on every zone update
  Optional: governor polling via module parameter
Resume re-programs the hardware: the cached threshold is invalidated on THERMAL_TZ_RESUME
11

## Slide 10
Not Intel-specific: ARM SCMI as a provider
Nothing in the interface is a PTC register. Two values, one registration.
thermal_zoneN (SCMI sensor) thermal_zone3 (int340x)
policy = hardware policy = hardware
│ │
└────────► gov_hardware ◄──────────┘
│ thermal_hw_gov_ops
┌──────────────┴──────────────┐
▼ ▼
SCMI thermal agent platform_temperature_control.c
│ │
▼ ▼
SCP / platform firmware PTC hardware loop
Both values are already SCMI commands — Sensor Management, protocol 0x15:
set_threshold(tz, temp) → SENSOR_TRIP_POINT_CONFIG (0x5), i.e.
scmi_sensor_proto_ops::trip_point_config()
— in tree today, with zero callers
set_temperature(tz, temp) → SENSOR_INJECT_READING — optional command,
an agent supplies a reading the platform
cannot take itself. Spec only: the enum in
arm_scmi/sensors.c stops at AXIS_NAME_GET.
Or left out entirely, where the platform
can read the sensor itself.
THERMAL_TEMP_INVALID → disable the trip point / notification
mitigation → PERFORMANCE_LIMITS_SET, powercap CAP_SET,
whatever the firmware owns — governor does
not care
SCMI temperature sensors already register real thermal zones (devm_thermal_of_zone_register(), drivers/hwmon/scmi-hwmon.c), so echo hardware > thermal_zoneN/policy needs no new user-space ABI there either
What SCMI would ask of the API:
• set_temperature optional — firmware that reads its own sensors only needs the threshold. Registration requires both callbacks today
• Callbacks may need to sleep — an SCMI transfer is a mailbox round trip. Under tz->lock that stalls the zone; a deferred/queued variant may be the right answer for such providers
12

## Slide 11
Locking and lifetime
tz->lock ───► hw_gov_lock (never the reverse)
• bind_to_tz / manage / unbind_from_tz all run under tz->lock
• Callbacks are invoked with tz->lock held, sometimes also hw_gov_lock → hardware driver may only take its own lock
• Driver unbind vs. zone teardown: remove from the pool first, then get_device() the zone, re-validate the owner under both locks
• No governor-private work item, so nothing to cancel under tz->lock
13

## Slide 12
Status
Code Link: https://git.kernel.org/pub/scm/linux/kernel/git/spandruvada/linux.git/log/?h=thermal-hardware-gov
CONFIG_THERMAL_GOV_HARDWARE=y
# echo 1000 > /sys/module/thermal_sys/parameters/hardware_polling_delay_ms
# cd /sys/class/thermal/thermal_zone3
# cat available_policies
hardware power_allocator user_space step_wise bang_bang fair_share
# echo hardware > policy
# cat policy
hardware
# thermal-threshold add 3 50000
That is the whole setup. Three steps:
• the polling interval — only for zones nothing else updates
• the policy — hands the zone to the hardware
• a threshold — becomes the hardware's target, programmed synchronously
# grep . /sys/bus/pci/devices/0000:00:04.0/ptc_*/thermal_zone
ptc_0_control/thermal_zone:thermal_zone3
ptc_1_control/thermal_zone:none
ptc_2_control/thermal_zone:none
• drivers/thermal/gov_hardware.c — governor + registration API
• platform_temperature_control.c — first user
• tools/thermal/thermal-threshold — thresholds have no sysfs interface
15